## Slide 1
TETRA-RTU and TETRA-Modem
TMO-100
Funk-Electronic Piciorgros GmbH Michael D. Piciorgros (CEO)

## Slide 2
Information Source
www.TetraModem.com

## Slide 3
Funk-Electronic Piciorgros GmbH
(TETRA Business)
Wireless Solutions from 1982 until 2023++
Member of the TETRA Association (MoU/TandCCA)
Core Manufacturer (Own TETRA Terminal)
IOP certified from ISCOM (Italy)
Member of the SME Group

## Slide 4
Funk-Electronic Piciorgros GmbH
(TMC-200 / T-One Terminal)
350, 380, 410, 450, 800 MHz
Status, SDS, Packet Data, MSPD
Authentication, Encryption,
TEA1, 2, 3

## Slide 5
Funk-Electronic Piciorgros GmbH
(National Approvals)
EU (BABT Certificate)
Hong Kong, Thailand, Russia
FCC (USA), IC (Canada)
Philippines, Australia, Malaysia

## Slide 7
Funk-Electronic Piciorgros GmbH
(IOP Certificates)
Rohill
SELEX
EADS / Cassidian
3T-Frequentis (Sepura)
Damm, Motorola
Teltronics
Hytera, (ETELM)

## Slide 10
TMO-100 = Tetra MOdem -100
Second Generation
Professional TETRA
Data Modem with Voice Option

## Slide 11: Typical SCADA Server Layout
Ref:
Scada: Wikipedia
Monitor: Samsung

## Slide 12
TETRA Modem - TMO-100 with two serial Ports, one Ethernet Port and an optional Audio Port

## Slide 13: TETRA Modem - TMO-100 as before with additional embedded I/O

## Slide 14: Power Supply: 12 Volt up to 24 Volt +/-20%

## Slide 15: Heavy Duty Connectors

## Slide 16: DIN-Rail Mounting

## Slide 17: SMA Antenna Connector

## Slide 18: 16 digital Inputs including … 8 Event Counter and 8 Timer (*) All inputs visible as LED

## Slide 19: 8 (16) digital Outputs PNP open Collector (500 mA each) All Outputs visible as LED

## Slide 20: 4 analog Inputs 0-20 mA or 4-20 mA

## Slide 21: 8 LED Field Strength Bar Graph indicating –dBm values

## Slide 22: Antenna Match LED (AMA) Indicates no, or faulty connected Antenna

## Slide 23: Two Serial Ports on top (D-Sub) RS-232 or RS-485 / (RS-422)

## Slide 24: 10/100 MB Ethernet Port

## Slide 25: Connector for Microphone/Speaker (Hardware Option)

## Slide 26: Large Variaty of Expansion Modules (Hardware Option)
Notes: 26

## Slide 27: TETRA Data Network Structure Radio-to-Radio

## Slide 28
SCADA using based Radio-to-Radio Communication
SDS
SCADA Control Room
Tetra Switch
PLC / RTU
Command and Control Device
Public Lighting
Serial Communication
TMO-100
TMO-100
TMO-100
SDS
SDS
SDS
SDS
TMO-100
Serial Interface
Serial Interface
I/O
Notes: 28

## Slide 29: TMO-100 TETRA Data Modem Network Structure Data Gateway-to-Radio

## Slide 30: Highly Redundant TETRA Packet Data Gateway for SCADA Critical Operation

## Slide 31: Highly Redundant TETRA Packet Data Gateway for SCADA Critical Operation
Supported Protocols:
MODBUS-RTU
IEC60870-5-101
DNP3
ROC
BSAP
PakBus
Siemens SINAUT
any customer specific or proprietary protocols

## Slide 32: Highly Redundant TETRA Packet Data Gateway for SCADA Critical Operation
Features:
COM Ports:
RS-232 or RS-485/422, Subin-D pole female
AUX Ports:
RS-232 or RS-485, RJ12 pole female
Ethernet Ports:
One (TGW-100) or two (TGW-100R)
Ethernet interfaces:
RJ-45, 10/100 MBps
Power Supply
Dual Power Supplies – hot swappable
Enclosure dimensions:
Complete 19" rack approx: 48,4 * 13,2 * 33 cm (no cables included)

## Slide 33
SCADA – using an
Control Room
TETRA Switch
AMR
Command and Control Line Device
Public Lighting
TGW-100 SDS Gateway
Two Serial Interfaces
IP Communication
TMO-100
TMO-100
TMO-100
SDS Gateway
SDS
SDS
SDS
I/O

## Slide 34: Performance Test with SDS-Gateway on ONE SCCH/MCCH:
Infrastructure: TETRA with one carrier
TETRA Data Link: One SCCH
Data Compression: OFF
Data nodes: One or more polling nodes, polling 10 TMO-100 each
Protocol: Modbus RTU
Polling Target: Polling different numbers of bytes from inside the TMO-100
 | One Node | Two Nodes | Three Nodes | Four Nodes | Eight Nodes
SDS: 20 Bytes | 65 | 130 | 240 | 250 | 295
SDS: 100 Bytes |  |  |  |  | 285
SDS: 200 Bytes |  |  |  |  | 265
Table showing polls per minute |  |  |  |  | 
Notes: 34

## Slide 35: Performance Test with SDS-Gateway on FOUR SCCH/MCCH:
Infrastructure: TETRA with one carrier
TETRA Data Link: MCCH plus three SCCH
Data Compression: OFF
Data nodes: One or more polling nodes, polling 10 TMO-100 each
Protocol: Modbus RTU
Polling Target: Polling different numbers of bytes from inside the TMO-100
 | One Node (on each TS) | Two Nodes (on each TS) | Three Nodes (on each TS) | Four Nodes (on each TS) | 16 Nodes (on each TS)
SDS: 20 Bytes | 210 | 400 | 600 | 760 | 980
SDS: 100 Bytes |  |  |  |  | 
SDS: 200 Bytes |  |  |  |  | 
Table showing total polls (on all time slots) per minute (values rounded) |  |  |  |  | 
Notes: 35

## Slide 36
Analog and Digital I/O
SCADA – using a Gateway
Tetra Switch
PLC / RTU
Command and Control Line Device
TGW-100 SDS Gateway
Two Serial Interfaces
IP Communication
TMO-100
TMO-100
TMO-100
PD
PD
PD
I/O
… or Serial Interface
Serial Interface
SCADA Control Room
Packet Data

## Slide 37
SCADA – using direct Communication
Tetra Switch
AMR, PLC or RTU
Command and Control Line Device
Direct IP Communication
TMO-100
TMO-100
TMO-100
IP
IP
IP
PD
PD
PD
I/O
SCADA Control Room

## Slide 38
Analog and Digital I/O
SCADA – using a Gateway
PLC / RTU
Command and Control Line Device
TMO-100
TMO-100
TMO-100
PD
PD
PD
I/O
… or Serial Interface
Serial Interface
Packet Data
TETRA Switch
TGW-100 SDS Gateway
IP Commu-nication
PLC / PRTU
PLC / PRTU
PLC / PRTU
PLC / PRTU
SCADA Control Room

## Slide 39: TMO-100 TETRA Data Modem Feature List

## Slide 40: Embedded Web-Browser

## Slide 41: Embedded IP and TETRA Router

## Slide 42: PLE - Powerful Java Graphic Editor

## Slide 43: No Cryptic Formulas for Logic design

## Slide 44: Powerful embedded Micro PLC

## Slide 45: TMO-100 TETRA Data Modem Features

## Slide 46: TMO-100 - TETRA related Features
SDS can be up to 255 bytes (2047 Bit) long. Type TL and TL 4
Packet Switched Data (IP) supported
Packet Data Channel Sharing supported
Single and Multi Slot Packet Data supported
Secondary Control Channel supported
Automatic PPP Link set up to the TETRA Switch
Router Function with Port Forwarding and NAT
Up to 3 Watt RF Output Power
Encryption, Authentication
Voice feature even with active Packet Data Link
Build in Tetra Monitor (local and remote) via embedded Web Server
Calibrated Field Strength Indicator on the Front Panel
Short Data or SDS can be sent as alarms (low field strength ...)
350 MHz, 380 MHz, 410 MHz 450 MHz and 800 MHz available

## Slide 47: TMO-100 – Voice Option
Standard 8 Pin Connector for Mic. Speaker handset
One Group Number (GISSI) to be programmed
Eight individual Numbers (ISSI) to be programmed
ISSI and GISSI to be programmed locally or remotely using the embedded Web Server
Select ISSI / GISSI by Voice Handset
Automatic PPP disconnect when pressing PTT
Automatic PPP re connect after Voice timeout or reject

## Slide 48: TMO-100 – Protocol and I/O related Features
All digital and analog I/O isolated
Serial Port COM / AUX available as RS-232 or RS-485/(422)
Level 1 Protocol: Timeout or 3964R
Serial Protocols can be sent via SDS or Packet Data (SoIP)
IP Protocols can be sent via Packet Data or SDS (IPoSDS)
Device Protocol to access internal Registers: Modbus RTU, Modbus IP, IEC60870-5-101, IEC60870-5-104
Serial Protocols to be forwarded:
Modbus RTU, DNP3, IEC 60870-5-101, PakBus, BSAP, ROC, … user Defined …
Ethernet 10/100 MBit IP-Port for Local Network
UDP and TCP supported
Embedded Web Server as Configuration Tool
Modbus/IP, IEC 60870-5-104 (!), DNP3/IP, … others …
Low Power Consumption: <3 Watt

## Slide 49: PicoLogo™ – User Application Interface
Easy to use graphical user interface
Optimized for Tetra Infrastructure
Basic Logic Functions (and, or, exor, … )
Complex Logic Functions (delay on, delay off, flip flop, …)
Analog Functions (analog compare, … )
Timer and Clock Functions (time, date,
Dynamic Text Message generation for Alarms and Status
GPS Functions (position, … )
Modbus RTU Slave (set and read register, coil, … )
Modbus RTU Master (set and read register, coil, … )
E-Mail send (sending text and alarm messages by e-mail)
SNMP Trap (automated machine messaging)
… more …

## Slide 50: TMO-100 – Embedded Web Server
Web Server to be used as …
Configuration Tool for the Device, Protocols and IP Parameter,
Configuration Tool for TETRA Network Parameter,
Configuration for the Voice Option
TETRA Monitor
Device Monitor
Error Log
Web Server can be accessed locally using the IP Port and remotely over the TETRA Infrastructure
Easy to be used with any Web Browser (Firefox, Internet Explorer, … )

## Slide 51: TMO-100 TETRA Data Modem Unique Features

## Slide 52: TMO-100
Feature rich All in One SCADA and Telemetry Solution
TETRA-Modem and TETRA-RTU
Interfaces fit the User Requirements and User Protocols (no ATDT .... Commands)
Embedded WEB Server
Embedded IP Router
Optional build in Digital and Analog I/O
Optional Voice Feature
Field proven in many applications
IOP approved for most of the existing infrastructures
IC and FCC approval
3 Watt RF power output in 350 – 470 MHz range
DIN Rail Mounting and 12-24 Volt DC +/-20% power supply
New: Over The Air Upgrade of Modem and TETRA Stack

## Slide 53
Typical SCADA Applications:
Notes: 53

## Slide 54: Open Pit Mining (Water Level Control)

## Slide 55: Turkey, Mining Application – DMO Mode

## Slide 56: ME, Gas and Oil

## Slide 57: Asia, Utility (Energy Companies) Pole Mounted Switches
Notes: 57

## Slide 59: Thank you very much for your interest in our Products
Funk - Electronic Piciorgros GmbH
Claudiastr. 5
51145 Köln-Porz
Germany
www.piciorgros.com
www.TetraModem.com